••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
X-Plane, by Austin Meyer
Simulating Aircraft/Extra Aircraft/ASG29_B21/ASG29_B21.acf
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••

x location positive aft x force positive right pitch/alpha pos nose up
y location positive right y force positive up roll pos right
z location positive up z force positive aft yaw/beta pos nose right

elevator, aileron, spoiler positive control surface up
rudder positive control surface right
drag-yaw positive control surface deployed
pitch cyclic prop pitch positive request nose up
roll cyclic prop pitch positive request nose right

Finite-Wing & Element Build-Up for LEFT WING 1:
root lo Re: B21_ASG29 (lo hi Re).afl
root hi Re: B21_ASG29 (lo hi Re).afl
tip lo Re: B21_ASG29 (lo hi Re).afl
tip hi Re: B21_ASG29 (lo hi Re).afl
Element # 0: S= 3.5864 sqr mtrs, MAC= 0.67 mtrs, incidence= 4.0 deg
Wing area for this wing= 3.5864
NOTE! I AM ADDING LEFT WING 2 TO THE TIP OF LEFT WING 1 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=4.9236)
NOTE! I AM ADDING LEFT WING 3 TO THE TIP OF LEFT WING 1 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for RIGT WING 1:
root lo Re: B21_ASG29 (lo hi Re).afl
root hi Re: B21_ASG29 (lo hi Re).afl
tip lo Re: B21_ASG29 (lo hi Re).afl
tip hi Re: B21_ASG29 (lo hi Re).afl
Element # 0: S= 3.5864 sqr mtrs, MAC= 0.67 mtrs, incidence= 4.0 deg
Wing area for this wing= 3.5864
NOTE! I AM ADDING RIGT WING 2 TO THE TIP OF RIGT WING 1 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=4.9236)
NOTE! I AM ADDING RIGT WING 3 TO THE TIP OF RIGT WING 1 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for LEFT WING 2:
root lo Re: B21_ASG29 (lo hi Re).afl
root hi Re: B21_ASG29 (lo hi Re).afl
tip lo Re: B21_ASG29 (lo hi Re).afl
tip hi Re: B21_ASG29 (lo hi Re).afl
Element # 0: S= 1.3372 sqr mtrs, MAC= 0.43 mtrs, incidence= 4.0 deg
Wing area for this wing= 1.3372
NOTE! I AM ADDING LEFT WING 1 TO THE ROOT OF LEFT WING 2 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=4.9236)
NOTE! I AM ADDING LEFT WING 3 TO THE TIP OF LEFT WING 2 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for RIGT WING 2:
root lo Re: B21_ASG29 (lo hi Re).afl
root hi Re: B21_ASG29 (lo hi Re).afl
tip lo Re: B21_ASG29 (lo hi Re).afl
tip hi Re: B21_ASG29 (lo hi Re).afl
Element # 0: S= 1.3372 sqr mtrs, MAC= 0.43 mtrs, incidence= 4.0 deg
Wing area for this wing= 1.3372
NOTE! I AM ADDING RIGT WING 1 TO THE ROOT OF RIGT WING 2 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=4.9236)
NOTE! I AM ADDING RIGT WING 3 TO THE TIP OF RIGT WING 2 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for LEFT WING 3:
root lo Re: B21_symmetrical.afl
root hi Re: B21_symmetrical.afl
tip lo Re: B21_symmetrical.afl
tip hi Re: B21_symmetrical.afl
Element # 0: S= 0.0502 sqr mtrs, MAC= 0.20 mtrs, incidence= 0.0 deg
Element # 1: S= 0.0374 sqr mtrs, MAC= 0.15 mtrs, incidence= 0.0 deg
Wing area for this wing= 0.0876
NOTE! I AM ADDING LEFT WING 2 TO THE ROOT OF LEFT WING 3 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=1.4248)
NOTE! I AM ADDING LEFT WING 1 TO THE ROOT OF LEFT WING 3 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for RIGT WING 3:
root lo Re: B21_symmetrical.afl
root hi Re: B21_symmetrical.afl
tip lo Re: B21_symmetrical.afl
tip hi Re: B21_symmetrical.afl
Element # 0: S= 0.0502 sqr mtrs, MAC= 0.20 mtrs, incidence= 0.0 deg
Element # 1: S= 0.0374 sqr mtrs, MAC= 0.15 mtrs, incidence= 0.0 deg
Wing area for this wing= 0.0876
NOTE! I AM ADDING RIGT WING 2 TO THE ROOT OF RIGT WING 3 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=1.4248)
NOTE! I AM ADDING RIGT WING 1 TO THE ROOT OF RIGT WING 3 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=5.0112)
After any wing-joining, our area is 5.01 m.
After any wing-joining, our semi-length is 8.84 m.
After any wing-joining, our root chord is 0.77 m.
After any wing-joining, our tip chord is 0.12 m.
After any wing-joining, our leading-edge sweep is 4.3 deg.
After any wing-joining, our mean aero sweep is 3.2 deg.
After any wing-joining, our aspect ratio is 31.0563.
After any wing-joining, spanwise centroid is 0.4468 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.6871.
After any wing-joining, our delta-wing ratio is 0.0000.
Oswalds efficiency is therefore 0.9363

Finite-Wing & Element Build-Up for LEFT H STAB:
root lo Re: NACA 0012 (symmetrical).afl
root hi Re: NACA 0012 (symmetrical).afl
tip lo Re: NACA 0009 (symmetrical).afl
tip hi Re: NACA 0009 (symmetrical).afl
Element # 0: S= 0.3906 sqr mtrs, MAC= 0.35 mtrs, incidence= -3.0 deg
Wing area for this wing= 0.3906
NOTE! I AM ADDING VERT STAB 1 TO THE ROOT OF LEFT H STAB (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=1.3518)
After any wing-joining, our area is 1.35 m.
After any wing-joining, our semi-length is 1.68 m.
After any wing-joining, our root chord is 0.93 m.
After any wing-joining, our tip chord is 0.22 m.
After any wing-joining, our leading-edge sweep is 13.6 deg.
After any wing-joining, our mean aero sweep is 7.7 deg.
After any wing-joining, our aspect ratio is 4.1097.
After any wing-joining, spanwise centroid is 0.4885 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.9325.
After any wing-joining, our delta-wing ratio is 0.0088.
Oswalds efficiency is therefore 0.9878

Finite-Wing & Element Build-Up for RIGT H STAB:
root lo Re: NACA 0012 (symmetrical).afl
root hi Re: NACA 0012 (symmetrical).afl
tip lo Re: NACA 0009 (symmetrical).afl
tip hi Re: NACA 0009 (symmetrical).afl
Element # 0: S= 0.3906 sqr mtrs, MAC= 0.35 mtrs, incidence= -3.0 deg
Wing area for this wing= 0.3906
NOTE! I AM ADDING VERT STAB 1 TO THE ROOT OF RIGT H STAB (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=1.3518)
After any wing-joining, our area is 1.35 m.
After any wing-joining, our semi-length is 1.68 m.
After any wing-joining, our root chord is 0.93 m.
After any wing-joining, our tip chord is 0.22 m.
After any wing-joining, our leading-edge sweep is 13.6 deg.
After any wing-joining, our mean aero sweep is 7.7 deg.
After any wing-joining, our aspect ratio is 4.1097.
After any wing-joining, spanwise centroid is 0.4885 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.9325.
After any wing-joining, our delta-wing ratio is 0.0088.
Oswalds efficiency is therefore 0.9878

Finite-Wing & Element Build-Up for VERT STAB 1:
root lo Re: NACA 64(2)-015_3m.afl
root hi Re: NACA 64(2)-015_9m.afl
tip lo Re: NACA 64(2)-015_3m.afl
tip hi Re: NACA 64(2)-015_9m.afl
Element # 0: S= 0.9612 sqr mtrs, MAC= 0.81 mtrs, incidence= 0.0 deg
Wing area for this wing= 0.9612
NOTE! I AM ADDING LEFT H STAB TO THE TIP OF VERT STAB 1 (through any intermediate wings) TO FORM ONE CONTINUOUS WING! (S=1.3518)
After any wing-joining, our area is 1.35 m.
After any wing-joining, our semi-length is 1.68 m.
After any wing-joining, our root chord is 0.93 m.
After any wing-joining, our tip chord is 0.22 m.
After any wing-joining, our leading-edge sweep is 13.6 deg.
After any wing-joining, our mean aero sweep is 7.7 deg.
After any wing-joining, our aspect ratio is 4.1097.
After any wing-joining, spanwise centroid is 0.4885 semi-spans. (this is area centroid fraction of the way out to the tip)
After any wing-joining, our taper ratio is 0.9325.
After any wing-joining, our delta-wing ratio is 0.0088.
Oswalds efficiency is therefore 0.9878

Critical altitude= 0 ft, rho at crit alt= 1.2250 kg/mmm, rho at SL= 1.2250 kg/mmm, engine power boosted to 1.0000 of original

After LEFT WING 1, the RUNNING TOTAL wetted area is 3.5864 square meters for all wings listed so far
After RIGT WING 1, the RUNNING TOTAL wetted area is 7.1729 square meters for all wings listed so far
After LEFT WING 2, the RUNNING TOTAL wetted area is 8.5101 square meters for all wings listed so far
After RIGT WING 2, the RUNNING TOTAL wetted area is 9.8473 square meters for all wings listed so far
After LEFT WING 3, the RUNNING TOTAL wetted area is 9.9349 square meters for all wings listed so far
After RIGT WING 3, the RUNNING TOTAL wetted area is 10.0225 square meters for all wings listed so far
After LEFT H STAB, the RUNNING TOTAL wetted area is 10.4131 square meters for all wings listed so far
After RIGT H STAB, the RUNNING TOTAL wetted area is 10.8037 square meters for all wings listed so far
After VERT STAB 1, the RUNNING TOTAL wetted area is 11.7649 square meters for all wings listed so far

Now for MI from FUSELAGE:
The frontal area is 0.4293 square meters
The side area is 2.4606 square meters
The top area is 2.0559 square meters
The lateral centroid is 0.00 meters
The vertical centroid is -0.06 meters
The longitudinal centroid for lift at 0 alpha is 0.03 meters
The longitudinal centroid for lift at 90 alpha is 0.03 meters
The longitudinal centroid for side force at 0 beta is 0.03 meters
The longitudinal centroid for side force at 90 beta is 0.03 meters
The RUNNING TOTAL wetted area is 18.9289 square meters, for the entire craft, including all wings, top and bottom surfaces, and all bodies listed so far
The RUNNING TOTAL radius of gyration in roll is 2.83 meters
The RUNNING TOTAL radius of gyration in pitch is 1.30 meters
The RUNNING TOTAL radius of gyration in yaw is 3.03 meters

As specified in the manual radius of gyration in the Weight and Balance screen in Plane Maker:
The radius of gyration in roll is 2.56 m
The radius of gyration in pitch is 0.91 m
The radius of gyration in yaw is 0.76 m

The centroid of all wings is at 0.26 m (positive aft from CG)
The average chord of all wings is 0.71 m
The static margin is 0.36 (positive stable, in mean aero chords of wings)

Critical altitude= 0 ft, rho at crit alt= 1.2250 kg/mmm, rho at SL= 1.2250 kg/mmm, engine power boosted to 1.0000 of original

Engine # 0, is mass 186.54 kg at x= 0.00, y= 0.17, z= -2.44

Prop # 0, is mass 4.33 kg at x= 0.00, y= 0.17, z= -2.44

After LEFT WING 1, the RUNNING TOTAL wetted area is 5.4701 square meters for all wings listed so far
After RIGT WING 1, the RUNNING TOTAL wetted area is 10.9403 square meters for all wings listed so far
After LEFT WING 2, the RUNNING TOTAL wetted area is 11.6985 square meters for all wings listed so far
After RIGT WING 2, the RUNNING TOTAL wetted area is 12.4567 square meters for all wings listed so far
After LEFT H STAB, the RUNNING TOTAL wetted area is 14.0175 square meters for all wings listed so far
After RIGT H STAB, the RUNNING TOTAL wetted area is 15.5783 square meters for all wings listed so far
After VERT STAB 1, the RUNNING TOTAL wetted area is 17.4268 square meters for all wings listed so far

Critical altitude= 0 ft, rho at crit alt= 1.2250 kg/mmm, rho at SL= 1.2250 kg/mmm, engine power boosted to 1.0000 of original

Engine # 0, is mass 142.88 kg at x= 0.00, y= -0.06, z= -2.14

Prop # 0, is mass 9.07 kg at x= 0.00, y= -0.06, z= -2.14

After LEFT WING 1, the RUNNING TOTAL wetted area is 3.3817 square meters for all wings listed so far
After RIGT WING 1, the RUNNING TOTAL wetted area is 6.7633 square meters for all wings listed so far
After LEFT WING 2, the RUNNING TOTAL wetted area is 10.6430 square meters for all wings listed so far
After RIGT WING 2, the RUNNING TOTAL wetted area is 14.5226 square meters for all wings listed so far
After LEFT WING 3, the RUNNING TOTAL wetted area is 14.8684 square meters for all wings listed so far
After RIGT WING 3, the RUNNING TOTAL wetted area is 15.2142 square meters for all wings listed so far
After LEFT H STAB, the RUNNING TOTAL wetted area is 17.0046 square meters for all wings listed so far
After RIGT H STAB, the RUNNING TOTAL wetted area is 18.7950 square meters for all wings listed so far
After VERT STAB 1, the RUNNING TOTAL wetted area is 20.3737 square meters for all wings listed so far

====================================================================================================
====================================================================================================
===AT TIME= 197.01 FLAPS 0 =====================================================================
====================================================================================================
====================================================================================================
flight control ptch: 0.1538 ratio
flight control hdng: 0.0009 ratio
flight control roll:-0.0008 ratio

h : 873 m
rho : 1.1251 kg/cubic meter, density ratio: 0.9184
vx : 26.5
vy : -1.2
vz : -8.9
mach-1 : 337.0 m/s
airspeed: 33.7 m/s
mach : 0.1001

psi : 76.2 deg
the : 1.5 deg
phi : -1.3 deg

alpha : 3.6 deg (pos nose up)
beta : 0.1 deg (pos nose right)

P : -0.1 deg/second
Q : -0.4 deg/second
R : -0.4 deg/second

tire height above ground : 873 m
resting height of aircraft above ground: 0 m

LEFT WING 1 height above ground: 874.07 m
hgt_in_cords is 1137.9735
hgt_in_spans is 49.4655
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 1 height above ground: 874.20 m
hgt_in_cords is 1138.1373
hgt_in_spans is 49.4726
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT WING 2 height above ground: 874.19 m
hgt_in_cords is 1533.7384
hgt_in_spans is 49.4723
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 2 height above ground: 874.52 m
hgt_in_cords is 1534.3152
hgt_in_spans is 49.4909
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT H STAB height above ground: 874.40 m
hgt_in_cords is 1912.5018
hgt_in_spans is 259.9227
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT H STAB height above ground: 874.42 m
hgt_in_cords is 1912.5608
hgt_in_spans is 259.9308
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

----------------------------------------------------------------------------------------------------
---RUNNING PROPULSIVE FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM---------------------------
----------------------------------------------------------------------------------------------------
Before all propulsion:
f_axil= 0.0 N, pos aft, L= 0.0 N-m, pos right
f_side= 0.0 N, pos right, M= 0.0 N-m, pos up
f_nrml= 0.0 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.6 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 3.6
incidence : 4.0
incidence increase : 0.0
geometric alpha : 7.6
v for forces : 33.7 (based on effective sweep of -1.0 deg)

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #1
That's the table for Re= 1.4000 million, with flight Re= 1.4454 million
alpha airflow= 7.6, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.3
Cl lookup: 0.9190
Cd lookup: 0.0076
Cm lookup: -0.0414

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.4000 1.4000 |
        reyno 2 1.4000 1.4000 |======>with flight Re= 1.4454 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.9190 0.9190 |
        reyno 2 0.9190 0.9190 |======>resultant cl= 0.9190

CD coeff summary: ---------- -root --tip
        reyno 1 0.0076 0.0076 |
        reyno 2 0.0076 0.0076 |======>resultant cd= 0.0076

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0414 -0.0414 |
        reyno 2 -0.0414 -0.0414 |======>resultant cm=-0.0414

finite-wing lift multiplier of 0.9801 takes cl to 0.9007, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0090

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.9053* 3.5864* sqr( 33.7) * 1.1251 / 2 = 2074.9 N
drag= 0.0165* 3.5864* sqr( 33.7) * 1.1251 / 2 = 37.9 N
momt=-0.0416* 3.5864* sqr( 33.7) * 1.1251 / 2 * 0.67= -64.2 N-m

LEFT WING 1:

x= -2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2074.9 N pos up.
drag_local_path= 37.9 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0511 0.9967 -0.0623
drag vector xyz= 0.0020 0.0623 0.9981
side vector xyz= 0.9987 -0.0512 0.0012

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 1
f_axil= -91.4 N, pos aft, L= 5614.9 N-m, pos right
f_side= 106.2 N, pos right, M= -135.3 N-m, pos up
f_nrml= 2070.5 N, pos up, N= 240.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 3.5
incidence : 4.0
incidence increase : 0.0
geometric alpha : 7.5
v for forces : 33.7 (based on effective sweep of 1.0 deg)

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #1
That's the table for Re= 1.4000 million, with flight Re= 1.4470 million
alpha airflow= 7.5, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.2
Cl lookup: 0.9164
Cd lookup: 0.0076
Cm lookup: -0.0414

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.4000 1.4000 |
        reyno 2 1.4000 1.4000 |======>with flight Re= 1.4470 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.9164 0.9164 |
        reyno 2 0.9164 0.9164 |======>resultant cl= 0.9164

CD coeff summary: ---------- -root --tip
        reyno 1 0.0076 0.0076 |
        reyno 2 0.0076 0.0076 |======>resultant cd= 0.0076

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0414 -0.0414 |
        reyno 2 -0.0414 -0.0414 |======>resultant cm=-0.0414

finite-wing lift multiplier of 0.9801 takes cl to 0.8981, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0089

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.9027* 3.5864* sqr( 33.7) * 1.1251 / 2 = 2073.5 N
drag= 0.0165* 3.5864* sqr( 33.7) * 1.1251 / 2 = 37.9 N
momt=-0.0416* 3.5864* sqr( 33.7) * 1.1251 / 2 * 0.67= -64.4 N-m

RIGT WING 1:

x= 2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2073.5 N pos up.
drag_local_path= 37.9 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0512 0.9968 -0.0618
drag vector xyz= 0.0020 0.0620 0.9981
side vector xyz= 0.9987 0.0509 -0.0052

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 1
f_axil= -181.8 N, pos aft, L= 3.9 N-m, pos right
f_side= 0.2 N, pos right, M= -270.1 N-m, pos up
f_nrml= 4139.6 N, pos up, N= 2.7 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.6 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 3.6
incidence : 4.0
incidence increase : 0.0
geometric alpha : 7.6
v for forces : 33.6 (based on effective sweep of -3.4 deg)

   AILERON #1: crat= 0.1500, def= -0.0 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te =-0.0001
al_inc=-0.0030
cl inc=-0.0008
cd inc= 0.0000
cm inc= 0.0005

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.9145 million
alpha airflow= 7.6, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.3
Cl lookup: 1.0268
Cd lookup: 0.0078
Cm lookup: -0.0414

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.9145 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.0268 1.0268 |
        reyno 2 1.0268 1.0268 |======>resultant cl= 1.0268

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0414 -0.0414 |
        reyno 2 -0.0414 -0.0414 |======>resultant cm=-0.0414

adding control-effects cl of -0.0008 takes cl to 1.0260
adding control-effects cd of 0.0000 takes cd to 0.0078
adding control-effects cm of 0.0005 takes cm to -0.0408
finite-wing lift multiplier of 0.9801 takes cl to 1.0056, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0112

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.0107* 1.3372* sqr( 33.6) * 1.1251 / 2 = 859.2 N
drag= 0.0190* 1.3372* sqr( 33.6) * 1.1251 / 2 = 16.1 N
momt=-0.0410* 1.3372* sqr( 33.6) * 1.1251 / 2 * 0.43= -14.9 N-m

LEFT WING 2:

x= -7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 859.2 N pos up.
drag_local_path= 16.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0485 0.9969 -0.0625
drag vector xyz= 0.0020 0.0625 0.9980
side vector xyz= 0.9988 -0.0486 0.0010

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 2
f_axil= -219.4 N, pos aft, L= 6045.1 N-m, pos right
f_side= 41.9 N, pos right, M= -447.5 N-m, pos up
f_nrml= 4997.2 N, pos up, N= 258.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 3.5
incidence : 4.0
incidence increase : 0.0
geometric alpha : 7.5
v for forces : 33.7 (based on effective sweep of 3.4 deg)

   AILERON #1: crat= 0.1500, def= 0.0 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te = 0.0001
al_inc= 0.0030
cl inc= 0.0008
cd inc= 0.0000
cm inc=-0.0005

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.9171 million
alpha airflow= 7.5, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.2
Cl lookup: 1.0208
Cd lookup: 0.0078
Cm lookup: -0.0414

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.9171 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.0208 1.0208 |
        reyno 2 1.0208 1.0208 |======>resultant cl= 1.0208

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0414 -0.0414 |
        reyno 2 -0.0414 -0.0414 |======>resultant cm=-0.0414

adding control-effects cl of 0.0008 takes cl to 1.0216
adding control-effects cd of 0.0000 takes cd to 0.0078
adding control-effects cm of -0.0005 takes cm to -0.0419
finite-wing lift multiplier of 0.9801 takes cl to 1.0012, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0111

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.0063* 1.3372* sqr( 33.7) * 1.1251 / 2 = 860.4 N
drag= 0.0189* 1.3372* sqr( 33.7) * 1.1251 / 2 = 16.1 N
momt=-0.0421* 1.3372* sqr( 33.7) * 1.1251 / 2 * 0.43= -15.4 N-m

RIGT WING 2:

x= 7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 860.4 N pos up.
drag_local_path= 16.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0486 0.9969 -0.0616
drag vector xyz= 0.0020 0.0617 0.9981
side vector xyz= 0.9988 0.0484 -0.0050

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 2
f_axil= -256.2 N, pos aft, L= -4.5 N-m, pos right
f_side= 0.2 N, pos right, M= -624.9 N-m, pos up
f_nrml= 5855.9 N, pos up, N= 7.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.6 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.1
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.1
v for forces : 30.4 (based on effective sweep of -22.0 deg)

AR=31.0607, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3839 million
alpha airflow= 1.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 1.0
Cl lookup: 0.1038
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3839 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.1038 0.1038 |
        reyno 2 0.1038 0.1038 |======>resultant cl= 0.1038

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.1018, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0607, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.1022* 0.0502* sqr( 30.4) * 1.1251 / 2 = 2.7 N
drag= 0.0011* 0.0502* sqr( 30.4) * 1.1251 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 30.4) * 1.1251 / 2 * 0.20= 0.0 N-m

LEFT WING 3:

x= -8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= 2.7 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9684 0.2487 -0.0175
drag vector xyz= 0.0020 0.0625 0.9980
side vector xyz= 0.2493 -0.9666 0.0600

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= -256.2 N, pos aft, L= 4.1 N-m, pos right
f_side= 2.8 N, pos right, M= -625.2 N-m, pos up
f_nrml= 5856.6 N, pos up, N= 7.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.6 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.1
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.1
v for forces : 30.4 (based on effective sweep of -22.0 deg)

AR=31.0607, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2873 million
alpha airflow= 1.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 1.0
Cl lookup: 0.1037
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2873 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.1037 0.1037 |
        reyno 2 0.1037 0.1037 |======>resultant cl= 0.1037

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.1017, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0607, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.1021* 0.0374* sqr( 30.4) * 1.1251 / 2 = 2.0 N
drag= 0.0011* 0.0374* sqr( 30.4) * 1.1251 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 30.4) * 1.1251 / 2 * 0.15= 0.0 N-m

LEFT WING 3:

x= -8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= 2.0 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9684 0.2487 -0.0175
drag vector xyz= 0.0020 0.0625 0.9980
side vector xyz= 0.2493 -0.9666 0.0600

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= -256.2 N, pos aft, L= 11.1 N-m, pos right
f_side= 4.7 N, pos right, M= -625.4 N-m, pos up
f_nrml= 5857.1 N, pos up, N= 6.5 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.8
incidence : 0.0
incidence increase : 0.0
geometric alpha : 0.8
v for forces : 30.5 (based on effective sweep of 22.0 deg)

AR=31.0543, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3853 million
alpha airflow= 0.8, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 0.8
Cl lookup: 0.0792
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3853 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0792 0.0792 |
        reyno 2 0.0792 0.0792 |======>resultant cl= 0.0792

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.0776, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0543, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0779* 0.0502* sqr( 30.5) * 1.1251 / 2 = 2.0 N
drag= 0.0011* 0.0502* sqr( 30.5) * 1.1251 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 30.5) * 1.1251 / 2 * 0.20= 0.0 N-m

RIGT WING 3:

x= 8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= 2.0 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9689 0.2471 -0.0133
drag vector xyz= 0.0020 0.0616 0.9981
side vector xyz= 0.2475 0.9670 -0.0602

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= -256.2 N, pos aft, L= 4.5 N-m, pos right
f_side= 2.7 N, pos right, M= -625.5 N-m, pos up
f_nrml= 5857.6 N, pos up, N= 7.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.8
incidence : 0.0
incidence increase : 0.0
geometric alpha : 0.8
v for forces : 30.5 (based on effective sweep of 22.0 deg)

AR=31.0543, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2884 million
alpha airflow= 0.8, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 0.8
Cl lookup: 0.0792
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2884 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0792 0.0792 |
        reyno 2 0.0792 0.0792 |======>resultant cl= 0.0792

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.0776, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0543, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0780* 0.0374* sqr( 30.5) * 1.1251 / 2 = 1.5 N
drag= 0.0011* 0.0374* sqr( 30.5) * 1.1251 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 30.5) * 1.1251 / 2 * 0.15= 0.0 N-m

RIGT WING 3:

x= 8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= 1.5 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9689 0.2471 -0.0134
drag vector xyz= 0.0020 0.0616 0.9981
side vector xyz= 0.2475 0.9670 -0.0602

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= -256.2 N, pos aft, L= -0.9 N-m, pos right
f_side= 1.2 N, pos right, M= -625.7 N-m, pos up
f_nrml= 5858.0 N, pos up, N= 7.7 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 2.3 deg, at v= 33.7 m/s for vertical delta= -1.37 m/s
So speed is changed to vx= 0.0 vy= 0.7 vz= 33.7 m/s
So final speed is vx= 0.0 vy= 0.7 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.2
incidence : -3.0
incidence increase : 0.0
geometric alpha : -1.8
v for forces : 33.6 (based on effective sweep of -4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -4.3 deg: (pos down or extended, neg up)
dx_te = 0.9989
dy_te =-0.0300
al_inc=-1.3777
cl inc=-0.1873
cd inc= 0.0001
cm inc= 0.1030
Effective alpha increased -1.4 deg by all combined lift-incrementation devices up to final geo alpha of -3.2 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.7553 million
alpha airflow= -3.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -2.5
Cl lookup: -0.2968
Cd lookup: 0.0054
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.7553 million
alpha airflow= -3.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -2.5
Cl lookup: -0.2597
Cd lookup: 0.0054
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.7553 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.2968 -0.2597 |
        reyno 2 -0.2968 -0.2597 |======>resultant cl=-0.2783

CD coeff summary: ---------- -root --tip
        reyno 1 0.0054 0.0054 |
        reyno 2 0.0054 0.0054 |======>resultant cd= 0.0054

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.1873 takes cl to -0.4656
adding control-effects cd of 0.0001 takes cd to 0.0055
adding control-effects cm of 0.1030 takes cm to 0.1030
finite-wing lift multiplier of 0.8884 takes cl to -0.4136, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0135

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.4157* 0.3906* sqr( 33.6) * 1.1251 / 2 = -103.1 N
drag= 0.0191* 0.3906* sqr( 33.6) * 1.1251 / 2 = 4.7 N
momt= 0.1044* 0.3906* sqr( 33.6) * 1.1251 / 2 * 0.35= 9.2 N-m

LEFT H STAB:

x= -0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -103.1 N pos up.
drag_local_path= 4.7 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0014 0.9998 -0.0208
drag vector xyz= 0.0012 0.0208 0.9998
side vector xyz= 1.0000 0.0014 -0.0012

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT H STAB
f_axil= -249.4 N, pos aft, L= -59.9 N-m, pos right
f_side= 1.4 N, pos right, M= -226.1 N-m, pos up
f_nrml= 5755.0 N, pos up, N= 3.2 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
DOWNWASH from RIGT WING 1 el #0 is 2.3 deg, at v= 33.7 m/s for vertical delta= -1.37 m/s
So speed is changed to vx= 0.0 vy= 0.7 vz= 33.7 m/s
So final speed is vx= 0.0 vy= 0.7 vz= 33.7 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.2
incidence : -3.0
incidence increase : 0.0
geometric alpha : -1.8
v for forces : 33.6 (based on effective sweep of 4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -4.3 deg: (pos down or extended, neg up)
dx_te = 0.9989
dy_te =-0.0300
al_inc=-1.3777
cl inc=-0.1873
cd inc= 0.0001
cm inc= 0.1030
Effective alpha increased -1.4 deg by all combined lift-incrementation devices up to final geo alpha of -3.2 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.7554 million
alpha airflow= -3.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -2.5
Cl lookup: -0.2965
Cd lookup: 0.0054
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.7554 million
alpha airflow= -3.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -2.5
Cl lookup: -0.2594
Cd lookup: 0.0054
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.7554 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.2965 -0.2594 |
        reyno 2 -0.2965 -0.2594 |======>resultant cl=-0.2780

CD coeff summary: ---------- -root --tip
        reyno 1 0.0054 0.0054 |
        reyno 2 0.0054 0.0054 |======>resultant cd= 0.0054

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.1873 takes cl to -0.4653
adding control-effects cd of 0.0001 takes cd to 0.0055
adding control-effects cm of 0.1030 takes cm to 0.1030
finite-wing lift multiplier of 0.8884 takes cl to -0.4133, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0135

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.4154* 0.3906* sqr( 33.6) * 1.1251 / 2 = -103.0 N
drag= 0.0191* 0.3906* sqr( 33.6) * 1.1251 / 2 = 4.7 N
momt= 0.1044* 0.3906* sqr( 33.6) * 1.1251 / 2 * 0.35= 9.2 N-m

RIGT H STAB:

x= 0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -103.0 N pos up.
drag_local_path= 4.7 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0014 0.9998 -0.0208
drag vector xyz= 0.0012 0.0208 0.9998
side vector xyz= 1.0000 -0.0015 -0.0012

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT H STAB
f_axil= -242.5 N, pos aft, L= -0.9 N-m, pos right
f_side= 1.2 N, pos right, M= 173.3 N-m, pos up
f_nrml= 5652.2 N, pos up, N= 7.6 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••VERT STAB 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.00 m, pos right from CG
element y= 0.45 m, pos up from CG
element z= 3.64 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 2.4 deg, at v= 33.7 m/s for vertical delta= -1.43 m/s
So speed is changed to vx= 0.0 vy= 0.6 vz= 33.7 m/s
WAKEWASH from LEFT WING 1 el #0 with cd= 0.0076, dy_chords= 0.06, wake_width_chords= 0.12, wake_deficit_at_center= 0.0449, wake_deficit_here= 0.0208, speed ratio= 0.9895
So speed is changed to vx= 0.0 vy= 0.6 vz= 33.3 m/s
So final speed is vx= 0.0 vy= 0.6 vz= 33.3 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.1
incidence : 0.0
incidence increase : 0.0
geometric alpha : -0.1
v for forces : 32.7 (based on effective sweep of 9.9 deg)

   RUDDER #1: crat= 0.3000, def= 0.0 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te = 0.0001
al_inc= 0.0053
cl inc= 0.0009
cd inc= 0.0000
cm inc=-0.0006

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_3m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 1.6768 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0050
Cd lookup: 0.0054
Cm lookup: 0.0000

root hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.6768 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0050
Cd lookup: 0.0046
Cm lookup: 0.0000

tip hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.6768 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0050
Cd lookup: 0.0046
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 3.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 1.6768 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.0050 -0.0050 |
        reyno 2 -0.0050 -0.0050 |======>resultant cl=-0.0050

CD coeff summary: ---------- -root --tip
        reyno 1 0.0054 0.0054 |
        reyno 2 0.0046 0.0046 |======>resultant cd= 0.0054

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of 0.0009 takes cl to -0.0041
adding control-effects cd of 0.0000 takes cd to 0.0054
adding control-effects cm of -0.0006 takes cm to -0.0006
finite-wing lift multiplier of 0.8884 takes cl to -0.0036, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.0036* 0.9612* sqr( 32.7) * 1.1251 / 2 = -2.1 N
drag= 0.0054* 0.9612* sqr( 32.7) * 1.1251 / 2 = 3.1 N
momt=-0.0006* 0.9612* sqr( 32.7) * 1.1251 / 2 * 0.81= -0.3 N-m

VERT STAB 1:

x= -0.00 m pos right.
y= 0.45 m pos up.
z= 3.64 m pos aft.

lift_local_path= -2.1 N pos up.
drag_local_path= 3.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-1.0000 -0.0002 0.0012
drag vector xyz= 0.0012 0.0192 0.9998
side vector xyz=-0.0002 0.9998 -0.0192

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
VERT STAB 1
f_axil= -239.4 N, pos aft, L= 0.1 N-m, pos right
f_side= 3.3 N, pos right, M= 174.5 N-m, pos up
f_nrml= 5652.2 N, pos up, N= 0.2 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Now to find aspect-ratio multiplier for LEFT WING 1:
   el # 0, clQ= 1028.4, el arm= 0.50, clQ_total= 1028.4, clQ_x_arm= 514.2
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 1:
   el # 0, clQ= 1027.7, el arm= 0.50, clQ_total= 1027.7, clQ_x_arm= 513.9
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 2:
   el # 0, clQ= 1142.2, el arm= 0.50, clQ_total= 1142.3, clQ_x_arm= 571.1
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 2:
   el # 0, clQ= 1143.8, el arm= 0.50, clQ_total= 1143.8, clQ_x_arm= 571.9
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 3:
   el # 0, clQ= 94.4, el arm= 0.50, clQ_total= 94.5, clQ_x_arm= 47.2
   el # 1, clQ= 94.4, el arm= 1.50, clQ_total= 188.8, clQ_x_arm= 188.8
      loc= 0.4999, AR_mult= 1.0001

Now to find aspect-ratio multiplier for RIGT WING 3:
   el # 0, clQ= 72.6, el arm= 0.50, clQ_total= 72.6, clQ_x_arm= 36.3
   el # 1, clQ= 72.6, el arm= 1.50, clQ_total= 145.2, clQ_x_arm= 145.2
      loc= 0.5001, AR_mult= 0.9999

Now to find aspect-ratio multiplier for LEFT H STAB:
   el # 0, clQ= 469.0, el arm= 0.50, clQ_total= 469.1, clQ_x_arm= 234.5
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT H STAB:
   el # 0, clQ= 468.8, el arm= 0.50, clQ_total= 468.8, clQ_x_arm= 234.4
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for VERT STAB 1:
   el # 0, clQ= 3.9, el arm= 0.50, clQ_total= 3.9, clQ_x_arm= 2.0
      loc= 0.5000, AR_mult= 1.0000

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
FUSELAGE:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
lat arm of centroid from acf ref= 0.00 m pos right
vrt arm of centroid from acf ref= -0.06 m pos up
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with alpha, with arm running from 0.03 at 0 alpha to 0.03 at 90 alpha, currently 3.6 alpha
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with beta , with arm running from 0.03 at 0 beta to 0.03 at 90 beta , currently 0.1 beta

body front area = 0.4293 square meters
body side area for side force = 2.4606 square meters
body top area for lift force = 2.0559 square meters

infinite flow speed is vx of 0.1 vy of 2.1 vz of 33.7 m/s in aircraft body coordinates
So final speed is vx= 0.1 vy= 2.1 vz= 33.7 m/s in the aircraft axis coordinate system

mach multiplication = 1.0050, part_cd= 0.0080, cd_cylinder= 1.0050
air attacking aft from ahead= 33.7 m/s.
air attacking up from below = 2.1 m/s.
air attacking to the right = 0.1 m/s.
alph= 3.6
beta= 0.1
angl= 3.6
cl vert= 0.0583, ref area of 2.0559, v= 33.7, rho= 1.1251, SUBSONIC body force= 76.7 N
cl side= 0.0019, ref area of 2.4606, v= 33.7, rho= 1.1251, SUBSONIC body force= 2.9 N
cd_frnt= 0.0157, ref area of 0.4434, v= 33.7, rho= 1.1251, SUBSONIC body force= 4.5 N

THIS BODY AT MACH= 0.1001
body drag force= 4.5 N (is CD of 0.0162 based on frontal area)
body side force= 2.9 N (is CL of 0.0019 based on side area)
body lift force= 76.7 N (is CL of 0.0583 based on top area)

LIFT at the centroid for alpha:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 76.7 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LIFT at the centroid for alpha
f_axil= -244.2 N, pos aft, L= 0.1 N-m, pos right
f_side= 3.3 N, pos right, M= 172.2 N-m, pos up
f_nrml= 5728.8 N, pos up, N= 0.2 N-m, pos right
----------------------------------------------------------------------------------------------------

SIDE at the centroid for beta:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 2.9 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
SIDE at the centroid for beta
f_axil= -244.2 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 172.2 N-m, pos up
f_nrml= 5728.8 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

DRAG at the aero centroid:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 4.5 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
DRAG at the aero centroid
f_axil= -239.7 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 171.9 N-m, pos up
f_nrml= 5729.1 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #2, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0334 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 5.3 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 0.00 -0.18 3.80 m

landing gear:

x= 0.00 m pos right.
y= -0.18 m pos up.
z= 3.80 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 5.3 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -234.4 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 169.7 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #3, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.3 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= -8.87 0.44 -0.16 m

landing gear:

x= -8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.3 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -234.1 N, pos aft, L= 0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 169.9 N-m, pos up
f_nrml= 5729.4 N, pos up, N= -2.5 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #4, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.3 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 8.87 0.44 -0.16 m

landing gear:

x= 8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.3 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9981 -0.0621
drag vector xyz= 0.0020 0.0621 0.9981
side vector xyz= 1.0000 -0.0001 -0.0020
----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After water skimming forces:
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------
I am adding mass for the jett load! Adding 200.0 kg, at long= -0.09 lat= 0.00 vert= 0.00, and changing the moments to:
L= 0.0 N-m, pos right
M= -169.0 N-m, pos up
N= -0.2 N-m, pos right
----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After shifted mass forces:
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

I am adding mass for the fuel! Adding 0.0 kg, at long= -2.23 lat= 0.00 vert= -0.06, and changing the moments to:
L= 0.0 N-m, pos right
M= -169.1 N-m, pos up
N= -0.2 N-m, pos right

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After fuel mass forces:
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After engine sep mass forces:
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After weapon mass forces:
f_axil= -233.8 N, pos aft, L= -0.1 N-m, pos right
f_side= 6.3 N, pos right, M= 170.0 N-m, pos up
f_nrml= 5729.4 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••GRAND TOTALS AT END OF FORCE AND MOMENT BUILD-UP•••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••

•••FINAL PROPULSIVE (ENGINE) FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL GEAR FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)••••••••••••••••••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••••••••••
f_side = 6.3 N, pos right
f_vertical= 5729.4 N, pos up
f_axial = -233.8 N, pos aft

L = -0.1 N-m, pos right
M = 170.0 N-m, pos up
N = 0.1 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG FLIGTH PATH AXIS (pos aft/right/up)••••••••••••••••••••••••••••••
f_side = 6.8 N, pos right
f_lift = 5732.9 N, pos up
f_drag = 122.7 N, pos aft

•••FINAL FORCES BEFORE ASSYMETRIC LOADING EFFECTS, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••
f_side = 6.3 N, pos right
f_vertical= 5729.4 N, pos up
f_axial = -233.8 N, pos aft

L = -0.1 N-m, pos right
M = 0.9 N-m, pos up
N = -0.1 N-m, pos right

•••MASSES TO GET FROM FORCES TO ACCELERATIONS•••••••••••••••••••••••••••••••••••••••••••••••••••••••
mass = 599.2 kg (ice accretion will change mass and MI if present!
roll MI = 2616.6 kg-m-m... M/mi=accel in RADIANS per sec
pitch MI = 335.3 kg-m-m... M/mi=accel in RADIANS per sec
yaw MI = 233.3 kg-m-m... M/mi=accel in RADIANS per sec

•••FINAL TOTAL LINEAR ACCELS, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••••••
a_x= 0.1 m/ss
a_y= -0.2 m/ss
a_z= -0.3 m/ss

•••FINAL TOTAL ANGULAR ACCELS, ABOUT AIRCRAFT AXIS (pos right/up/right)•••••••••••••••••••••••••••••
Pdot (roll) = -0.0 deg/ss
Qdot (pitch)= 0.0 deg/ss
Rdot (yaw) = -0.0 deg/ss

•••FINAL TOTAL LINEAR VELOCITIES, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••
v_x= 26.5 m/s
v_y= -1.2 m/s
v_z= -8.9 m/s

====================================================================================================
====================================================================================================
===AT TIME= 255.40 FLAPS 4/A ================================================================
====================================================================================================
====================================================================================================
flight control ptch: 0.4012 ratio
flight control hdng:-0.0009 ratio
flight control roll:-0.0048 ratio

h : 838 m
rho : 1.1290 kg/cubic meter, density ratio: 0.9216
vx : 20.6
vy : -0.4
vz : 11.6
mach-1 : 337.1 m/s
airspeed: 29.6 m/s
mach : 0.0879

psi : 114.9 deg
the : 3.3 deg
phi : 0.1 deg

alpha : 4.0 deg (pos nose up)
beta : 0.1 deg (pos nose right)

P : -0.1 deg/second
Q : 0.7 deg/second
R : -0.1 deg/second

tire height above ground : 838 m
resting height of aircraft above ground: 0 m

LEFT WING 1 height above ground: 840.01 m
hgt_in_cords is 1093.6248
hgt_in_spans is 47.5377
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 1 height above ground: 840.00 m
hgt_in_cords is 1093.6083
hgt_in_spans is 47.5370
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT WING 2 height above ground: 840.24 m
hgt_in_cords is 1474.1622
hgt_in_spans is 47.5506
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT WING 2 height above ground: 840.20 m
hgt_in_cords is 1474.1045
hgt_in_spans is 47.5488
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

LEFT H STAB height above ground: 840.16 m
hgt_in_cords is 1837.6252
hgt_in_spans is 249.7465
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

RIGT H STAB height above ground: 840.16 m
hgt_in_cords is 1837.6191
hgt_in_spans is 249.7456
setting ground effect cl multiplier to 1.0001
setting ground effect cdi multiplier to 1.0000
setting ground effect wash multiplier to 1.0000

----------------------------------------------------------------------------------------------------
---RUNNING PROPULSIVE FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM---------------------------
----------------------------------------------------------------------------------------------------
Before all propulsion:
f_axil= 0.0 N, pos aft, L= 0.0 N-m, pos right
f_side= 0.0 N, pos right, M= 0.0 N-m, pos up
f_nrml= 0.0 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 4.0
incidence : 4.0
incidence increase : 0.0
geometric alpha : 8.0
v for forces : 29.6 (based on effective sweep of -1.0 deg)

   FLAPS #1: crat= 0.1400, def= 14.0 deg: (pos down or extended, neg up)
dx_te = 0.9958
dy_te = 0.0339
al_inc= 1.5644
cl inc= 0.2369
cd inc= 0.0009
cm inc=-0.2369
Effective alpha increased 1.6 deg by all combined lift-incrementation devices up to final geo alpha of 9.6 deg

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number:	Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using tables 0 and 1
That's the tables for Re= 1.1000 million and Re= 1.4000 million, with flight Re= 1.2742 million
alpha airflow= 9.6, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 9.2
alpha airflow= 9.6, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 9.2
Cl lookups: 1.2798 and 1.1064, interpolated Cl= 1.1791
Cd lookups: 0.0078 and 0.0086, interpolated Cd= 0.0083
Cm lookups: -0.0404 and -0.0404, interpolated Cm=-0.0404

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.2742 1.2742 |
        reyno 2 1.2742 1.2742 |======>with flight Re= 1.2742 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.1791 1.1791 |
        reyno 2 1.1791 1.1791 |======>resultant cl= 1.1791

CD coeff summary: ---------- -root --tip
        reyno 1 0.0083 0.0083 |
        reyno 2 0.0083 0.0083 |======>resultant cd= 0.0083

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0404 -0.0404 |
        reyno 2 -0.0404 -0.0404 |======>resultant cm=-0.0404

adding control-effects cl of 0.2369 takes cl to 1.4160
adding control-effects cd of 0.0009 takes cd to 0.0092
adding control-effects cm of -0.2369 takes cm to -0.2773
finite-wing lift multiplier of 0.9801 takes cl to 1.3878, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0213

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.3933* 3.5864* sqr( 29.6) * 1.1290 / 2 = 2476.2 N
drag= 0.0304* 3.5864* sqr( 29.6) * 1.1290 / 2 = 54.1 N
momt=-0.2783* 3.5864* sqr( 29.6) * 1.1290 / 2 * 0.67= -333.4 N-m

LEFT WING 1:

x= -2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2476.2 N pos up.
drag_local_path= 54.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0510 0.9962 -0.0705
drag vector xyz= 0.0014 0.0705 0.9975
side vector xyz= 0.9987 -0.0510 0.0022

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 1
f_axil= -120.5 N, pos aft, L= 6699.5 N-m, pos right
f_side= 126.3 N, pos right, M= -425.7 N-m, pos up
f_nrml= 2470.6 N, pos up, N= 304.6 N-m, pos right
----------------------------------------------------------------------------------------------------
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 2.68 m, pos right from CG
element y= 0.69 m, pos up from CG
element z= 0.00 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 4.0
incidence : 4.0
incidence increase : 0.0
geometric alpha : 8.0
v for forces : 29.6 (based on effective sweep of 1.0 deg)

   FLAPS #1: crat= 0.1400, def= 14.0 deg: (pos down or extended, neg up)
dx_te = 0.9958
dy_te = 0.0339
al_inc= 1.5644
cl inc= 0.2370
cd inc= 0.0009
cm inc=-0.2370
Effective alpha increased 1.6 deg by all combined lift-incrementation devices up to final geo alpha of 9.6 deg

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number:	Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using tables 0 and 1
That's the tables for Re= 1.1000 million and Re= 1.4000 million, with flight Re= 1.2743 million
alpha airflow= 9.6, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 9.2
alpha airflow= 9.6, alpha zero-lift= -0.5, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 9.2
Cl lookups: 1.2756 and 1.1033, interpolated Cl= 1.1755
Cd lookups: 0.0078 and 0.0086, interpolated Cd= 0.0083
Cm lookups: -0.0404 and -0.0404, interpolated Cm=-0.0404

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.2743 1.2743 |
        reyno 2 1.2743 1.2743 |======>with flight Re= 1.2743 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.1755 1.1755 |
        reyno 2 1.1755 1.1755 |======>resultant cl= 1.1755

CD coeff summary: ---------- -root --tip
        reyno 1 0.0083 0.0083 |
        reyno 2 0.0083 0.0083 |======>resultant cd= 0.0083

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0404 -0.0404 |
        reyno 2 -0.0404 -0.0404 |======>resultant cm=-0.0404

adding control-effects cl of 0.2370 takes cl to 1.4124
adding control-effects cd of 0.0009 takes cd to 0.0092
adding control-effects cm of -0.2370 takes cm to -0.2774
finite-wing lift multiplier of 0.9801 takes cl to 1.3843, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0211

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.3898* 3.5864* sqr( 29.6) * 1.1290 / 2 = 2470.4 N
drag= 0.0303* 3.5864* sqr( 29.6) * 1.1290 / 2 = 53.9 N
momt=-0.2785* 3.5864* sqr( 29.6) * 1.1290 / 2 * 0.67= -333.6 N-m

RIGT WING 1:

x= 2.68 m pos right.
y= 0.69 m pos up.
z= 0.00 m pos aft.

lift_local_path= 2470.4 N pos up.
drag_local_path= 53.9 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0510 0.9963 -0.0698
drag vector xyz= 0.0014 0.0700 0.9975
side vector xyz= 0.9987 0.0508 -0.0050

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 1
f_axil= -239.2 N, pos aft, L= 15.5 N-m, pos right
f_side= 0.4 N, pos right, M= -850.4 N-m, pos up
f_nrml= 4935.5 N, pos up, N= 4.7 N-m, pos right
----------------------------------------------------------------------------------------------------
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 4.1
incidence : 4.0
incidence increase : 0.0
geometric alpha : 8.1
v for forces : 29.6 (based on effective sweep of -3.4 deg)

   AILERON #1: crat= 0.1500, def= -0.1 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te =-0.0004
al_inc=-0.0174
cl inc=-0.0047
cd inc= 0.0000
cm inc= 0.0032
Effective alpha increased -0.0 deg by all combined lift-incrementation devices up to final geo alpha of 8.1 deg

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.8067 million
alpha airflow= 8.1, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.7
Cl lookup: 1.0880
Cd lookup: 0.0078
Cm lookup: -0.0411

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.8067 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.0880 1.0880 |
        reyno 2 1.0880 1.0880 |======>resultant cl= 1.0880

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0411 -0.0411 |
        reyno 2 -0.0411 -0.0411 |======>resultant cm=-0.0411

adding control-effects cl of -0.0047 takes cl to 1.0833
adding control-effects cd of 0.0000 takes cd to 0.0078
adding control-effects cm of 0.0032 takes cm to -0.0380
finite-wing lift multiplier of 0.9801 takes cl to 1.0617, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0124

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.0659* 1.3372* sqr( 29.6) * 1.1290 / 2 = 703.6 N
drag= 0.0202* 1.3372* sqr( 29.6) * 1.1290 / 2 = 13.4 N
momt=-0.0381* 1.3372* sqr( 29.6) * 1.1290 / 2 * 0.43= -10.8 N-m

LEFT WING 2:

x= -7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 703.6 N pos up.
drag_local_path= 13.4 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0480 0.9963 -0.0709
drag vector xyz= 0.0015 0.0709 0.9975
side vector xyz= 0.9988 -0.0480 0.0020

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 2
f_axil= -275.8 N, pos aft, L= 4960.4 N-m, pos right
f_side= 34.2 N, pos right, M= -999.5 N-m, pos up
f_nrml= 5637.5 N, pos up, N= 255.1 N-m, pos right
----------------------------------------------------------------------------------------------------
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 2 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 7.00 m, pos right from CG
element y= 0.91 m, pos up from CG
element z= 0.15 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 4.0
incidence : 4.0
incidence increase : 0.0
geometric alpha : 8.0
v for forces : 29.6 (based on effective sweep of 3.4 deg)

   AILERON #1: crat= 0.1500, def= 0.1 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te = 0.0004
al_inc= 0.0174
cl inc= 0.0047
cd inc= 0.0000
cm inc=-0.0032
Effective alpha increased 0.0 deg by all combined lift-incrementation devices up to final geo alpha of 8.0 deg

AR=31.0563, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_ASG29 (lo hi Re).afl, coefficient lookup, I have 2 Reynolds numbers available, and am using table #0
That's the table for Re= 1.1000 million, with flight Re= 0.8069 million
alpha airflow= 8.0, alpha zero-lift= -0.3, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 7.7
Cl lookup: 1.0822
Cd lookup: 0.0078
Cm lookup: -0.0412

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 1.1000 1.1000 |
        reyno 2 1.1000 1.1000 |======>with flight Re= 0.8069 million

CL coeff summary: ---------- -root --tip
        reyno 1 1.0822 1.0822 |
        reyno 2 1.0822 1.0822 |======>resultant cl= 1.0822

CD coeff summary: ---------- -root --tip
        reyno 1 0.0078 0.0078 |
        reyno 2 0.0078 0.0078 |======>resultant cd= 0.0078

CM coeff summary: ---------- -root --tip
        reyno 1 -0.0412 -0.0412 |
        reyno 2 -0.0412 -0.0412 |======>resultant cm=-0.0412

adding control-effects cl of 0.0047 takes cl to 1.0869
adding control-effects cd of 0.0000 takes cd to 0.0078
adding control-effects cm of -0.0032 takes cm to -0.0443
finite-wing lift multiplier of 0.9801 takes cl to 1.0652, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0563, gives cdi of 0.0125

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 1.0694* 1.3372* sqr( 29.6) * 1.1290 / 2 = 706.3 N
drag= 0.0203* 1.3372* sqr( 29.6) * 1.1290 / 2 = 13.4 N
momt=-0.0445* 1.3372* sqr( 29.6) * 1.1290 / 2 * 0.43= -12.6 N-m

RIGT WING 2:

x= 7.00 m pos right.
y= 0.91 m pos up.
z= 0.15 m pos aft.

lift_local_path= 706.3 N pos up.
drag_local_path= 13.4 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0481 0.9964 -0.0695
drag vector xyz= 0.0015 0.0697 0.9976
side vector xyz= 0.9988 0.0479 -0.0048

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 2
f_axil= -311.5 N, pos aft, L= -3.7 N-m, pos right
f_side= 0.3 N, pos right, M= -1150.0 N-m, pos up
f_nrml= 6342.2 N, pos up, N= 10.8 N-m, pos right
----------------------------------------------------------------------------------------------------
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.5 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.5 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.2
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.2
v for forces : 26.6 (based on effective sweep of -22.0 deg)

AR=31.0514, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3373 million
alpha airflow= 1.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 1.1
Cl lookup: 0.1140
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3373 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.1140 0.1140 |
        reyno 2 0.1140 0.1140 |======>resultant cl= 0.1140

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.1117, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0514, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.1121* 0.0502* sqr( 26.6) * 1.1290 / 2 = 2.3 N
drag= 0.0012* 0.0502* sqr( 26.6) * 1.1290 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 26.6) * 1.1290 / 2 * 0.20= 0.0 N-m

LEFT WING 3:

x= -8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= 2.3 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9682 0.2494 -0.0192
drag vector xyz= 0.0015 0.0711 0.9975
side vector xyz= 0.2501 -0.9658 0.0685

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= -311.6 N, pos aft, L= 3.7 N-m, pos right
f_side= 2.4 N, pos right, M= -1150.2 N-m, pos up
f_nrml= 6342.8 N, pos up, N= 10.3 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.5 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.5 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.2
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.2
v for forces : 26.6 (based on effective sweep of -22.0 deg)

AR=31.0514, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2524 million
alpha airflow= 1.2, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 1.1
Cl lookup: 0.1142
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2524 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.1142 0.1142 |
        reyno 2 0.1142 0.1142 |======>resultant cl= 0.1142

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.1119, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0514, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.1122* 0.0374* sqr( 26.6) * 1.1290 / 2 = 1.7 N
drag= 0.0012* 0.0374* sqr( 26.6) * 1.1290 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 26.6) * 1.1290 / 2 * 0.15= 0.0 N-m

LEFT WING 3:

x= -8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= 1.7 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.9682 0.2494 -0.0192
drag vector xyz= 0.0015 0.0712 0.9975
side vector xyz= 0.2501 -0.9658 0.0686

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT WING 3
f_axil= -311.6 N, pos aft, L= 9.6 N-m, pos right
f_side= 4.1 N, pos right, M= -1150.4 N-m, pos up
f_nrml= 6343.2 N, pos up, N= 9.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.68 m, pos right from CG
element y= 1.12 m, pos up from CG
element z= 0.30 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.0
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.0
v for forces : 26.7 (based on effective sweep of 22.0 deg)

AR=31.0596, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.3376 million
alpha airflow= 1.0, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 0.9
Cl lookup: 0.0943
Cd lookup: 0.0010
Cm lookup: 0.0000

element 1 of 2, center at 25%, which is 25% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.3376 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0943 0.0943 |
        reyno 2 0.0943 0.0943 |======>resultant cl= 0.0943

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.0924, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0596, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0927* 0.0502* sqr( 26.7) * 1.1290 / 2 = 1.9 N
drag= 0.0011* 0.0502* sqr( 26.7) * 1.1290 / 2 = 0.0 N
momt= 0.0000* 0.0502* sqr( 26.7) * 1.1290 / 2 * 0.20= 0.0 N-m

RIGT WING 3:

x= 8.68 m pos right.
y= 1.12 m pos up.
z= 0.30 m pos aft.

lift_local_path= 1.9 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9686 0.2481 -0.0159
drag vector xyz= 0.0015 0.0696 0.9976
side vector xyz= 0.2486 0.9662 -0.0678

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= -311.6 N, pos aft, L= 3.5 N-m, pos right
f_side= 2.3 N, pos right, M= -1150.5 N-m, pos up
f_nrml= 6343.7 N, pos up, N= 10.3 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT WING 3 ELEMENT # 1••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 8.74 m, pos right from CG
element y= 1.37 m, pos up from CG
element z= 0.40 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 1.0
incidence : 0.0
incidence increase : 0.0
geometric alpha : 1.0
v for forces : 26.7 (based on effective sweep of 22.0 deg)

AR=31.0596, e= 0.9363, ls_D_ls0= 0.9410, al_D_al0= 0.9601, cl_D_cl0= 0.9801

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/B21_symmetrical.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 0.2527 million
alpha airflow= 1.0, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.9601, slat alpha divisor= 1.0000, alpha lookup= 0.9
Cl lookup: 0.0942
Cd lookup: 0.0010
Cm lookup: 0.0000

element 2 of 2, center at 75%, which is 75% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 9.0000 9.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 0.2527 million

CL coeff summary: ---------- -root --tip
        reyno 1 0.0942 0.0942 |
        reyno 2 0.0942 0.0942 |======>resultant cl= 0.0942

CD coeff summary: ---------- -root --tip
        reyno 1 0.0010 0.0010 |
        reyno 2 0.0010 0.0010 |======>resultant cd= 0.0010

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

finite-wing lift multiplier of 0.9801 takes cl to 0.0923, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9363, geometric aspect ratio of 31.0563, effective aspect ratio of 31.0596, gives cdi of 0.0001

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift= 0.0926* 0.0374* sqr( 26.7) * 1.1290 / 2 = 1.4 N
drag= 0.0011* 0.0374* sqr( 26.7) * 1.1290 / 2 = 0.0 N
momt= 0.0000* 0.0374* sqr( 26.7) * 1.1290 / 2 * 0.15= 0.0 N-m

RIGT WING 3:

x= 8.74 m pos right.
y= 1.37 m pos up.
z= 0.40 m pos aft.

lift_local_path= 1.4 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.9686 0.2481 -0.0159
drag vector xyz= 0.0015 0.0696 0.9976
side vector xyz= 0.2486 0.9662 -0.0678

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT WING 3
f_axil= -311.6 N, pos aft, L= -1.4 N-m, pos right
f_side= 0.9 N, pos right, M= -1150.7 N-m, pos up
f_nrml= 6344.0 N, pos up, N= 10.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••LEFT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 3.6 deg, at v= 29.6 m/s for vertical delta= -1.86 m/s
So speed is changed to vx= 0.0 vy= 0.3 vz= 29.6 m/s
So final speed is vx= 0.0 vy= 0.3 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.5
incidence : -3.0
incidence increase : 0.0
geometric alpha : -2.5
v for forces : 29.5 (based on effective sweep of -4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -11.2 deg: (pos down or extended, neg up)
dx_te = 0.9923
dy_te =-0.0779
al_inc=-3.5939
cl inc=-0.4653
cd inc= 0.0008
cm inc= 0.2559
Effective alpha increased -3.6 deg by all combined lift-incrementation devices up to final geo alpha of -6.1 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.6650 million
alpha airflow= -6.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -4.7
Cl lookup: -0.5655
Cd lookup: 0.0066
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.6650 million
alpha airflow= -6.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -4.7
Cl lookup: -0.4948
Cd lookup: 0.0062
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.6650 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.5655 -0.4948 |
        reyno 2 -0.5655 -0.4948 |======>resultant cl=-0.5301

CD coeff summary: ---------- -root --tip
        reyno 1 0.0066 0.0062 |
        reyno 2 0.0066 0.0062 |======>resultant cd= 0.0064

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.4653 takes cl to -0.9955
adding control-effects cd of 0.0008 takes cd to 0.0071
adding control-effects cm of 0.2559 takes cm to 0.2559
finite-wing lift multiplier of 0.8884 takes cl to -0.8843, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0618

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.8877* 0.3906* sqr( 29.5) * 1.1290 / 2 = -170.2 N
drag= 0.0689* 0.3906* sqr( 29.5) * 1.1290 / 2 = 13.2 N
momt= 0.2589* 0.3906* sqr( 29.5) * 1.1290 / 2 * 0.35= 17.5 N-m

LEFT H STAB:

x= -0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -170.2 N pos up.
drag_local_path= 13.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-0.0006 1.0000 -0.0092
drag vector xyz= 0.0013 0.0092 1.0000
side vector xyz= 1.0000 0.0006 -0.0013

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LEFT H STAB
f_axil= -296.8 N, pos aft, L= -99.0 N-m, pos right
f_side= 1.0 N, pos right, M= -484.3 N-m, pos up
f_nrml= 6173.9 N, pos up, N= 1.8 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••RIGT H STAB ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= 0.57 m, pos right from CG
element y= 1.06 m, pos up from CG
element z= 3.72 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from RIGT WING 1 el #0 is 3.6 deg, at v= 29.6 m/s for vertical delta= -1.85 m/s
So speed is changed to vx= 0.0 vy= 0.3 vz= 29.6 m/s
So final speed is vx= 0.0 vy= 0.3 vz= 29.6 m/s in the aircraft axis coordinate system

alpha of the wing plane : 0.5
incidence : -3.0
incidence increase : 0.0
geometric alpha : -2.5
v for forces : 29.5 (based on effective sweep of 4.0 deg)

   ELEVATOR #1: crat= 0.4000, def= -11.2 deg: (pos down or extended, neg up)
dx_te = 0.9923
dy_te =-0.0779
al_inc=-3.5939
cl inc=-0.4653
cd inc= 0.0008
cm inc= 0.2559
Effective alpha increased -3.6 deg by all combined lift-incrementation devices up to final geo alpha of -6.1 deg

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0012 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 0.6649 million
alpha airflow= -6.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -4.7
Cl lookup: -0.5652
Cd lookup: 0.0066
Cm lookup: 0.0000

tip lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 0009 (symmetrical).afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 6.0000 million, with flight Re= 0.6649 million
alpha airflow= -6.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -4.7
Cl lookup: -0.4945
Cd lookup: 0.0062
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 6.0000 |
        reyno 2 3.0000 6.0000 |======>with flight Re= 0.6649 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.5652 -0.4945 |
        reyno 2 -0.5652 -0.4945 |======>resultant cl=-0.5298

CD coeff summary: ---------- -root --tip
        reyno 1 0.0066 0.0062 |
        reyno 2 0.0066 0.0062 |======>resultant cd= 0.0064

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.4653 takes cl to -0.9952
adding control-effects cd of 0.0008 takes cd to 0.0071
adding control-effects cm of 0.2559 takes cm to 0.2559
finite-wing lift multiplier of 0.8884 takes cl to -0.8841, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0618

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.8874* 0.3906* sqr( 29.5) * 1.1290 / 2 = -170.1 N
drag= 0.0689* 0.3906* sqr( 29.5) * 1.1290 / 2 = 13.2 N
momt= 0.2589* 0.3906* sqr( 29.5) * 1.1290 / 2 * 0.35= 17.5 N-m

RIGT H STAB:

x= 0.57 m pos right.
y= 1.06 m pos up.
z= 3.72 m pos aft.

lift_local_path= -170.1 N pos up.
drag_local_path= 13.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0006 1.0000 -0.0092
drag vector xyz= 0.0013 0.0092 1.0000
side vector xyz= 1.0000 -0.0007 -0.0013

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
RIGT H STAB
f_axil= -282.0 N, pos aft, L= -1.4 N-m, pos right
f_side= 1.0 N, pos right, M= 181.6 N-m, pos up
f_nrml= 6003.9 N, pos up, N= 10.6 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••VERT STAB 1 ELEMENT # 0••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
element x= -0.00 m, pos right from CG
element y= 0.45 m, pos up from CG
element z= 3.64 m, pos aft from CG

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
DOWNWASH from LEFT WING 1 el #0 is 3.7 deg, at v= 29.6 m/s for vertical delta= -1.93 m/s
So speed is changed to vx= 0.0 vy= 0.2 vz= 29.6 m/s
WAKEWASH from LEFT WING 1 el #0 with cd= 0.0092, dy_chords= 0.05, wake_width_chords= 0.14, wake_deficit_at_center= 0.0499, wake_deficit_here= 0.0340, speed ratio= 0.9829
So speed is changed to vx= 0.0 vy= 0.2 vz= 29.1 m/s
So final speed is vx= 0.0 vy= 0.2 vz= 29.1 m/s in the aircraft axis coordinate system

alpha of the wing plane : -0.1
incidence : 0.0
incidence increase : 0.0
geometric alpha : -0.1
v for forces : 28.6 (based on effective sweep of 9.9 deg)

   RUDDER #1: crat= 0.3000, def= -0.0 deg: (pos down or extended, neg up)
dx_te = 1.0000
dy_te =-0.0001
al_inc=-0.0053
cl inc=-0.0010
cd inc= 0.0000
cm inc= 0.0006

AR= 4.1097, e= 0.9878, ls_D_ls0= 0.6900, al_D_al0= 0.7767, cl_D_cl0= 0.8884

root lo Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_3m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 3.0000 million, with flight Re= 1.4701 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0062
Cd lookup: 0.0054
Cm lookup: 0.0000

root hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.4701 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0062
Cd lookup: 0.0046
Cm lookup: 0.0000

tip hi Reynolds number: Aircraft/Extra Aircraft/ASG29_B21/airfoils/NACA 64(2)-015_9m.afl, coefficient lookup, I have 1 Reynolds numbers available, and am using table #0
That's the table for Re= 9.0000 million, with flight Re= 1.4701 million
alpha airflow= -0.1, alpha zero-lift= -0.0, finite wing alpha multiplier= 0.7767, slat alpha divisor= 1.0000, alpha lookup= -0.1
Cl lookup: -0.0062
Cd lookup: 0.0046
Cm lookup: 0.0000

element 1 of 1, center at 50%, which is 50% of foil interpolation span (at foil interp power of 1.0000)

Re summary: ---------- -root --tip
        reyno 1 3.0000 3.0000 |
        reyno 2 9.0000 9.0000 |======>with flight Re= 1.4701 million

CL coeff summary: ---------- -root --tip
        reyno 1 -0.0062 -0.0062 |
        reyno 2 -0.0062 -0.0062 |======>resultant cl=-0.0062

CD coeff summary: ---------- -root --tip
        reyno 1 0.0054 0.0054 |
        reyno 2 0.0046 0.0046 |======>resultant cd= 0.0054

CM coeff summary: ---------- -root --tip
        reyno 1 0.0000 0.0000 |
        reyno 2 0.0000 0.0000 |======>resultant cm= 0.0000

adding control-effects cl of -0.0010 takes cl to -0.0071
adding control-effects cd of 0.0000 takes cd to 0.0054
adding control-effects cm of 0.0006 takes cm to 0.0006
finite-wing lift multiplier of 0.8884 takes cl to -0.0063, OLD FLIGHT MODEL, MODDING CONTROL EFFECTS AS WELL. EXPERIMENTAL FLIGHT MODEL WILL PUT THIS BEFORE CONTROL EFFECTS
e of 0.9878, geometric aspect ratio of 4.1097, effective aspect ratio of 4.1097, gives cdi of 0.0000

force along the local flight path of this particular element (see Aifoil-Maker plots in the 'AOA-180' tab to see sign conventions)
lift=-0.0064* 0.9612* sqr( 28.6) * 1.1290 / 2 = -2.8 N
drag= 0.0054* 0.9612* sqr( 28.6) * 1.1290 / 2 = 2.4 N
momt= 0.0006* 0.9612* sqr( 28.6) * 1.1290 / 2 * 0.81= 0.2 N-m

VERT STAB 1:

x= -0.00 m pos right.
y= 0.45 m pos up.
z= 3.64 m pos aft.

lift_local_path= -2.8 N pos up.
drag_local_path= 2.4 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz=-1.0000 -0.0002 0.0013
drag vector xyz= 0.0013 0.0066 1.0000
side vector xyz=-0.0002 1.0000 -0.0066

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
VERT STAB 1
f_axil= -279.6 N, pos aft, L= -0.1 N-m, pos right
f_side= 3.8 N, pos right, M= 182.6 N-m, pos up
f_nrml= 6003.9 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Now to find aspect-ratio multiplier for LEFT WING 1:
   el # 0, clQ= 1223.1, el arm= 0.50, clQ_total= 1223.1, clQ_x_arm= 611.6
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 1:
   el # 0, clQ= 1220.3, el arm= 0.50, clQ_total= 1220.3, clQ_x_arm= 610.1
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 2:
   el # 0, clQ= 932.2, el arm= 0.50, clQ_total= 932.2, clQ_x_arm= 466.1
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT WING 2:
   el # 0, clQ= 935.7, el arm= 0.50, clQ_total= 935.7, clQ_x_arm= 467.9
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for LEFT WING 3:
   el # 0, clQ= 79.5, el arm= 0.50, clQ_total= 79.5, clQ_x_arm= 39.8
   el # 1, clQ= 79.6, el arm= 1.50, clQ_total= 159.2, clQ_x_arm= 159.2
      loc= 0.5002, AR_mult= 0.9998

Now to find aspect-ratio multiplier for RIGT WING 3:
   el # 0, clQ= 65.9, el arm= 0.50, clQ_total= 65.9, clQ_x_arm= 33.0
   el # 1, clQ= 65.8, el arm= 1.50, clQ_total= 131.8, clQ_x_arm= 131.7
      loc= 0.4999, AR_mult= 1.0001

Now to find aspect-ratio multiplier for LEFT H STAB:
   el # 0, clQ= 772.1, el arm= 0.50, clQ_total= 772.1, clQ_x_arm= 386.0
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for RIGT H STAB:
   el # 0, clQ= 771.6, el arm= 0.50, clQ_total= 771.6, clQ_x_arm= 385.8
      loc= 0.5000, AR_mult= 1.0000

Now to find aspect-ratio multiplier for VERT STAB 1:
   el # 0, clQ= 5.2, el arm= 0.50, clQ_total= 5.2, clQ_x_arm= 2.6
      loc= 0.5000, AR_mult= 1.0000

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
FUSELAGE:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
lat arm of centroid from acf ref= 0.00 m pos right
vrt arm of centroid from acf ref= -0.06 m pos up
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with alpha, with arm running from 0.03 at 0 alpha to 0.03 at 90 alpha, currently 4.0 alpha
lon arm of centroid from acf ref= 0.03 m pos aft, for vertical force with beta , with arm running from 0.03 at 0 beta to 0.03 at 90 beta , currently 0.1 beta

body front area = 0.4293 square meters
body side area for side force = 2.4606 square meters
body top area for lift force = 2.0559 square meters

infinite flow speed is vx of 0.0 vy of 2.1 vz of 29.6 m/s in aircraft body coordinates
So final speed is vx= 0.0 vy= 2.1 vz= 29.6 m/s in the aircraft axis coordinate system

mach multiplication = 1.0039, part_cd= 0.0080, cd_cylinder= 1.0039
air attacking aft from ahead= 29.6 m/s.
air attacking up from below = 2.1 m/s.
air attacking to the right = 0.0 m/s.
alph= 4.0
beta= 0.1
angl= 4.0
cl vert= 0.0658, ref area of 2.0559, v= 29.6, rho= 1.1290, SUBSONIC body force= 67.1 N
cl side= 0.0013, ref area of 2.4606, v= 29.6, rho= 1.1290, SUBSONIC body force= 1.6 N
cd_frnt= 0.0175, ref area of 0.4468, v= 29.6, rho= 1.1290, SUBSONIC body force= 3.9 N

THIS BODY AT MACH= 0.0879
body drag force= 3.9 N (is CD of 0.0183 based on frontal area)
body side force= 1.6 N (is CL of 0.0013 based on side area)
body lift force= 67.1 N (is CL of 0.0658 based on top area)

LIFT at the centroid for alpha:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 67.1 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
LIFT at the centroid for alpha
f_axil= -284.4 N, pos aft, L= -0.1 N-m, pos right
f_side= 3.8 N, pos right, M= 180.7 N-m, pos up
f_nrml= 6070.8 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

SIDE at the centroid for beta:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.0 N pos aft.
side_local_path= 1.6 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
SIDE at the centroid for beta
f_axil= -284.4 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 180.7 N-m, pos up
f_nrml= 6070.8 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

DRAG at the aero centroid:

x= 0.00 m pos right.
y= -0.06 m pos up.
z= 0.03 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 3.9 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
DRAG at the aero centroid
f_axil= -280.5 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 180.4 N-m, pos up
f_nrml= 6071.1 N, pos up, N= 0.1 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #2, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0334 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 4.1 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 0.00 -0.18 3.80 m

landing gear:

x= 0.00 m pos right.
y= -0.18 m pos up.
z= 3.80 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 4.1 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -276.3 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.6 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #3, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.2 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= -8.87 0.44 -0.16 m

landing gear:

x= -8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -276.1 N, pos aft, L= -0.0 N-m, pos right
f_side= 5.4 N, pos right, M= 178.7 N-m, pos up
f_nrml= 6071.4 N, pos up, N= -2.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Landing gear #4, deployed 1.0000:
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
STRUT area exposed (including actuating struts if retract)= 0.0000 square meters
TIRES area exposed (tire may be largely hidden by fairing)= 0.0019 square meters
DOORS area exposed (all gear doors, 0 for fixed-gear) = 0.0000 square meters
STRUT Cd = 0.0500
TIRES Cd = 0.2500
DOORS Cd = 0.0000
drag of exposed STRUT = 0.0 N
drag of exposed TIRES = 0.2 N
drag of exposed DOORS = 0.0 N
drag of this gear from additional drag from Plane-Maker = 0.0 N
X/Y/Z= 8.87 0.44 -0.16 m

landing gear:

x= 8.87 m pos right.
y= 0.44 m pos up.
z= -0.16 m pos aft.

lift_local_path= 0.0 N pos up.
drag_local_path= 0.2 N pos aft.
side_local_path= 0.0 N pos right.

lift vector xyz= 0.0000 0.9975 -0.0702
drag vector xyz= 0.0014 0.0702 0.9975
side vector xyz= 1.0000 -0.0001 -0.0014
----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
landing gear
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After water skimming forces:
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------
I am adding mass for the jett load! Adding 200.0 kg, at long= -0.09 lat= 0.00 vert= 0.00, and changing the moments to:
L= 0.0 N-m, pos right
M= -179.2 N-m, pos up
N= -0.2 N-m, pos right

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After shifted mass forces:
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------
I am adding mass for the fuel! Adding 0.0 kg, at long= -2.23 lat= 0.00 vert= -0.06, and changing the moments to:
L= 0.0 N-m, pos right
M= -179.2 N-m, pos up
N= -0.2 N-m, pos right

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After fuel mass forces:
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After engine sep mass forces:
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

----------------------------------------------------------------------------------------------------
---RUNNING AERODYNAMIC FORCE AND TOTAL MOMENT TOTALS, AIRCRAFT AXIS SYSTEM--------------------------
----------------------------------------------------------------------------------------------------
After weapon mass forces:
f_axil= -275.9 N, pos aft, L= -0.2 N-m, pos right
f_side= 5.4 N, pos right, M= 178.8 N-m, pos up
f_nrml= 6071.4 N, pos up, N= 0.0 N-m, pos right
----------------------------------------------------------------------------------------------------

••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
•••GRAND TOTALS AT END OF FORCE AND MOMENT BUILD-UP•••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••

•••FINAL PROPULSIVE (ENGINE) FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL GEAR FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)••••••••••••••••••••••••••••••••••••••••
f_side = 0.0 N, pos right
f_vertical= 0.0 N, pos up
f_axial = 0.0 N, pos aft

L = 0.0 N-m, pos right
M = 0.0 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••••••••••••••••••••••••
f_side = 5.4 N, pos right
f_vertical= 6071.4 N, pos up
f_axial = -275.9 N, pos aft

L = -0.2 N-m, pos right
M = 178.8 N-m, pos up
N = 0.0 N-m, pos right

•••FINAL AERODYNAMIC FORCES, ALONG FLIGTH PATH AXIS (pos aft/right/up)••••••••••••••••••••••••••••••
f_side = 5.7 N, pos right
f_lift = 6075.8 N, pos up
f_drag = 151.1 N, pos aft

•••FINAL FORCES BEFORE ASSYMETRIC LOADING EFFECTS, ALONG AIRCRAFT AXIS (pos aft/right/up)•••••••••••
f_side = 5.4 N, pos right
f_vertical= 6071.4 N, pos up
f_axial = -275.9 N, pos aft

L = -0.2 N-m, pos right
M = -0.4 N-m, pos up
N = -0.1 N-m, pos right

•••MASSES TO GET FROM FORCES TO ACCELERATIONS•••••••••••••••••••••••••••••••••••••••••••••••••••••••
mass = 599.2 kg (ice accretion will change mass and MI if present!
roll MI = 2616.6 kg-m-m... M/mi=accel in RADIANS per sec
pitch MI = 335.3 kg-m-m... M/mi=accel in RADIANS per sec
yaw MI = 233.3 kg-m-m... M/mi=accel in RADIANS per sec

•••FINAL TOTAL LINEAR ACCELS, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••••••
a_x= -0.1 m/ss
a_y= 0.3 m/ss
a_z= -0.1 m/ss

•••FINAL TOTAL ANGULAR ACCELS, ABOUT AIRCRAFT AXIS (pos right/up/right)•••••••••••••••••••••••••••••
Pdot (roll) = -0.0 deg/ss
Qdot (pitch)= -0.0 deg/ss
Rdot (yaw) = -0.0 deg/ss

•••FINAL TOTAL LINEAR VELOCITIES, ALONG GLOBAL AXIS (pos south/east/up)•••••••••••••••••••••••••••••
v_x= 20.6 m/s
v_y= -0.4 m/s
v_z= 11.6 m/s